## Slide 1: Time-Division Multiplexing for FPGA Considering CNN Model Switch Time IEEE IPDPS Workshop - AsHES Tetsuro Nakamura, NTT Network Service Lab.

## Slide 2: Agenda
Ⅰ. INTRODUCTION
  Edge computing / System requirements
Ⅱ. ANALYSIS FOR ACCELERATOR SHARING
  Target usecase / CNN acceleration on FPGA / Time-division multiplex FPGA
Ⅲ. MACHINE PRE-EVLUATION FOR FEASIBILITY
  CNN model switch cost on FPGA / Optimization difficulties per CNN models
Ⅳ. PROPOSED METHOD
  System architecture / Scheduling algorithm
Ⅴ. EVALUATION
  User Performance / Fairness among users / Resource efficiency
Ⅵ. CONCLUSIONS and FUTURE WORK

## Slide 3: Ⅰ. INTRODUCTION – Edge Computing
Can’t we share FPGAs among users in Edge Computing?
Cloud to Edge Computing
  Improvement on Latency, Saving Network Traffic
  Any Improvement on Resource Efficiency ?
CPU to Heterogeneous Resources
  GPU
    High throughput / High Performance on Deep Neural Network
  FPGA
    Low Latency / Low Power Consumption
    Monolithic Design / Fixed Resource in Edge+Cloud
      Potential Low Utilization / Over-Provisioning

## Slide 4: Ⅰ. INTRODUCTION – System Requirements
System requirements to share FPGA among multiple users
Resource Efficiency
  Maximized Device Utilization
  Minimum Cost to Switch Device Users
Fairness between Users
  No monopolization of the shared device / No Resource Starvation
  Max-min Fairness
Real Time Performance
  Minimum Turn Around Time / Minimum Response Time
Hardware Abstraction
  Dynamic Resource Scale
  Brings Agility to Service

## Slide 5: Ⅱ. ANALYSIS FOR ACCELERATOR SHARING
Target Application / Use Case:
  Inference for Images / Video Streaming on Edge Server
  Convolutional Neural Network (CNN) Algorithm on FPGA
  Concurrent Requests from Multiple Users
What is CNN ?
  Deep Neural Network for Recognizing / Classifying Images
  Various CNN algorithm models with Different Layer Depths and Sizes
    Single Shot Detector (SSD): Object Detection
    Residual Network (ResNet): Image Classification

## Slide 6: Ⅱ. ANALYSIS FOR ACCELERATOR SHARING
Acceleration models of CNN algorithms on FPGA
  Fixed-Model Acceleration
    Static lay out of a CNN model on internal FPGA chip
    Effective Performance
    Less Flexibility
      Hardware reconfiguration necessary to switch CNN model
  Programmable-Model Acceleration
    Load CNN model on FPGA off-chip device memory
    More Flexibility
      Support concurrent requests of various kinds of CNN models
We focus on Programmable-Model Acceleration
to build Time-multiplexed FPGA sharing system

## Slide 7: Ⅱ. ANALYSIS FOR ACCELERATOR SHARING
How Programmable-Model CNN Accelerators work
FPGA Chip
Conv
Pooling
Fully
FPGA Device memory
CNN Algorithm
Model Biases
Input:32x32x1
Conv1:28x28x20
Pooling1:14x14x20
Conv2:10x10x20
Pooling2:5x5x20
Conv3:3x3x20
Conv1
Fully:1x1x6
Pooling1
Conv2
Pooling2
Conv3
Fully
Input Matrix
Output Matrix
32x32x1
32x32x1
1x1x6
1x1x6
Parallel Processing
Hierarchical Loop
Model Information
Weights, Biases
Results
Input Matrix
Store Output
Load Input
Supported calculation
instructions
Common processing part by hardware chip
that can support various CNN models
Different between CNN algorithms and models
Host Memory
PCIe Bus

## Slide 8: Ⅱ. ANALYSIS FOR ACCELERATOR SHARING
Time-division sharing of FPGA device
  Support Context Save in FPGA
    Enables to preempt jobs at any time, as well as CPU
    Two ways to save FPGA context / state
      Inside FPGA : High *spatial* cost
      In host memory : High *time* cost
  No Context Save in FPGA
    Each Job assumed as non-preemptive
    Switch users at reasonable job granularity
      Switch users only when no state to save is retained internally in FPGA
      i.e. per inference execution for an image frame (～milliseconds)
We focus on no context save switch
(because actual inference time is short enough)

## Slide 9: Ⅲ. MACHINE PRE-EVLUATION FOR FEASIBILITY
Evaluated programmable-model accelerator with two CNN models
  Single Shot Detection (SSD)
    model size: 4.5 MB
    model switch time: 3.9 ms
    inference execution time: 20.62 ms
  Residual Network 50 (ResNet50)
    model size: 54 MB
    model switch time: 48.9 ms
    inference execution time: 11.58 ms
(Note: model switch time is the time to transfer the model parameter from host memory to device memory)
The first problem:
Model/User switch cost is not negligible compared to execution time
Hardware | Server | Dell R740 PowerEdge
 | CPU | Intel Xeon Gold 5118
 | Host Memory | 96 GB
 | FPGA | Xilinx Alveo U50LV
Software | OS | Ubuntu 18.04.4
 | Driver | XRT 2019.2
Table I. Evaluation Environment

## Slide 10: Ⅲ. MACHINE PRE-EVLUATION FOR FEASIBILITY
Throughput Analysis on Different CNN models
The second problem:
Model difference in the optimal number of FPGA execution threads
SSD needs three threads to maximize the throughput while ResNet50 doesn’t
Each model require detailed hardware tuning while the requirement of resource hardware abstraction prevents it.

## Slide 11: Ⅳ. PROPOSED METHOD – System Architecture
Switch cost is not negligible
→ New Algorithm Proposed:
  [Switch Aware WFQ]
  Minimizes Switch cost
  Ageing Technique with Weighted Fair Queuing
Difference among models
→ Thread Manager Integrated:
  Prepares thread groups for each model
  Pays out threads on demand to optimal numbers automatically

## Slide 12: Ⅳ. PROPOSED METHOD – Scheduling Algorithm
Existing Fair Scheduling Algorithms for CPU
  Complete Fair Scheduler, Multi-level Feed Back Queue
  Not suitable since they depend on CPU context switch
Weighted Fair Queueing (WFQ) Algorithm
  Used in area of network bandwidth control
  Select job with earliest virtual finish time
    Implicitly use ageing technique
    Prevent resource starvation
SAWFQ: switch-aware WFQ proposed
  Extension of WFQ to take switch cost into account
  Introduces virtual jobs for model switches
  “switch penalty”: the burst time of the virtual model switch jobs
Notes: .

## Slide 13: Ⅳ. PROPOSED METHOD – Scheduling Algorithm
How to Optimize the scheduler parameter “Switch Penalty”?
  We created SAWFQ simulator, simulated many times
  Finally found there is an optimal value for switch penalty
Simulated Two Cases:
  Periodic Arrival:
    Streaming Request
  Random Arrival:
    On Demand Request
Smaller switch penalty is faster,
but it bursts at an optimal point
Notes: .

## Slide 14: Ⅳ. PROPOSED METHOD – Scheduling Algorithm
Formulation of optimal Switch Penalty for CNN models
Job Request Interval:
  Job Request Rate:
Cycle period of all the model executions:
Amounts of executed jobs for a model in a cycle:
  Job Execution Rate:
time
Switch Time
Switch Time
Switch Time
jobs
Burst Condition: “execution rate larger than request rate”
  … (＊)
E.g. Switch between Two models:
Notes: .

## Slide 15: Ⅳ. PROPOSED METHOD – Scheduling Algorithm
time
Note WFQ calculates virtual time dividing actual time by weight (), so switch penalty () and switch time () are weighted in actual time
jobs
Then, the burst condition (＊) becomes
(
Notes: .

## Slide 16: Ⅴ. PEFORMANCE EVALUATION
Implemented the System of SAWFQ on FPGA
The System Evaluated with Traditional Algorithms
  FCFS (First Come First Served), RR (Round Robin)
Three Evaluation Points:
  User Performance
  Fairness Among Users
  Resource Efficiency
Two CNN Models on Programmable-Model Accelerator:
  SSD, ResNet50
  Each CNN user issues inference requests periodically
Hardware | Server | Dell R740 PowerEdge
 | CPU | Intel Xeon Gold 5118
 | Host Memory | 96 GB
 | FPGA | Xilinx Alveo U50LV
Software | OS | Ubuntu 18.04.4
 | Driver | XRT 2019.2
Table I. Evaluation Environment

## Slide 17: Ⅴ. EVALUATION – User Performance
Requirement (3) Real-Time
  Request Interval Time:
    SSD: 30ms , ResNet50: 55ms
    Load where Jobs have a little waiting time in queues
  Metrics1: Scheduling Overhead
    130-170 us
  Metrics2: Turn Around Time
Better performance - SAWFQ can minimize the switch costs since it is aware of switch time thanks to the concept of switch penalty
Model | Turnaround Time (ms) |  |  |  |  | 
 | SAWFQ |  | Round Robin |  | FCFS | 
 | Mean | Worst | Mean | Worst | Mean | Worst
SSD | 278 | 478 | 16,781 | 33,154 | 19,552 | 38,911
Resnet | 196 | 508 | 29,434 | 42,111 | 19,591 | 38,996

## Slide 18: Ⅴ. EVALUATION – Fairness Among Users
Requirement (2) Fairness Among Users
  Request Interval Time:
    SSD Low Load - SSD: 30ms , ResNet50: 55ms
    SSD High Load - SSD: 5ms , ResNet50: 55ms
  Metrics3: FPGA Total Utilization Time Ratio Between Users (Models)
    Why Not Total Utilization Time? - Waiting Time / Slowdown not suitable
      Waiting time orders differs too much between algorithms
Note 100 % is completely fair
FCFS:
  Vulnerable to request load
Round Robin:
  Robust to request load, but not good
  depends on the rate of one inference period of SSD vs. ResNet
SAWFQ:
  Min-max Fairness as well as WFQ

## Slide 19: Ⅴ. EVALUATION – Resource Efficiency
Requirement (1) Resource Efficiency
  Request Interval Time:
    SSD: 5ms , ResNet50: 55ms
    High load since it doesn’t make much sense to measure efficiency when there are little jobs to execute
  Metrics4: FPGA Utilization Rate Against Idle Time
    System (not user) Point of view
      Considers user (or model) switch time as idle time
 | SAWFQ | RR | FCFS
Device Utilization (%) | 75.72 | 44.93 | 42.80
Better efficiency - SAWFQ can minimize the switch costs since it is aware of switch time thanks to the concept of switch penalty

## Slide 20: Ⅵ. CONCLUSIONS and FUTURE WORK
Conclusions
  Proposed system…
    Enables multiple users to share an FPGA device by switching CNN models on FPGA memory device
    Integrates a thread manager to maximize the throughput without reveling hardware resource to users
    Integrates new scheduling algorithm, Switch-Aware WFQ, to provide high resource efficiency, real-time performance and user fairness.
Future work
  In this work, both FPGA chip and FPGA device memory are time-division multiplexed
  We’d like to make FPGA device memory spatial-division multiplexed to minimize the switch cost
    Dynamic assign of device memory for CNN models
    Extension of FPGA driver to limit memory space for a user process.